## Slide 1: Statistical Analysis for Aquatic Resource Spatial Survey Designs
Anthony (Tony) R. Olsen
USEPA NHEERL
Western Ecology Division
Corvallis, Oregon
Voice: (541) 754-4790
Email: olsen.tony@epa.gov

## Slide 2: Spatial Survey Design Process
Resource
Characteristics
Monitoring
Objectives
Institutional
Constraints
Design
Requirements
Target
Population
Sample
Frame
Spatial
Survey
Design
Site
Selection
using R
Design
File
Notes: Spatial survey design process involves three interrelated steps: (1) specifying the design requirements based on monitoring objectives, resource characteristics, target population, sample frame and institutional constraints, (2) selecting a spatial survey design that accomplishes the design requirements, and (3) selecting the sites based on the spatial survey design and the sample frame to produce the design file.

## Slide 3: Spatial Survey Designs: Statistical Analysis Process
Adjust planned survey design weights to reflect implemented survey design
Complete population estimates for aquatic resource extent (number, length, area) based on spatial units evaluated
  Target and non-target population extent in sample frame
  Target population sampled (sampled population) extent
  Non-target population extent in sample frame by reason why non-target
Complete population estimates for indicators based on spatial units sampled
  Continuous data: cumulative distribution functions, percentiles and means
  Categorical data: proportions
Complete population estimates of relative and attributable risk

## Slide 4: Statistical Computing Environment: Assumptions & Solution
Data file will be available as:
  CSV or tab delimited file
  Excel spreadsheet
Monitoring staff has
  Limited Time for statistical analyses
  Minimal statistical training related to survey analysis
Organization has limitations on software
  Specific statistical software adopted
  no option to purchase alternative
Solution: Adopt R Statistical Software
  Flexible statistical analysis environment
  Create package for survey analyses
  Open source software: free!

## Slide 5: R & spsurvey Operation Initial Step Each Project
Install R
Start R
Install sp & spsurvey libraries
  Only have to do this part once or whenever an updated library is available
Install Tinn-R (optional) as editor to use with R
Create a folder for each project
Place an “.Rdata” file in project folder
Start R by double clicking on “.Rdata” file
Start Tinn-R
Open an example spsurvey analysis script
Modify example script to complete population estimation for project

## Slide 6: Monitoring Statistical Analysis Information http://WWW.EPA.GOV/NHEERL/ARM
Go to Design & Analysis > Analysis Information
Three levels
  Overview of the analysis process for information from probability surveys, with examples
  Detailed information to guide analyses
  Example results and reporting methods
  Technical guidance and software to support statistical analyses and estimation procedures
Use spsurvey vignettes as examples
Bibliography: consult papers by Stevens and Olsen

## Slide 7: Adjust Weight & Spatial Unit Evaluation

## Slide 8: Spatial Unit (site) Evaluation Process
Spatial units in sample evaluated to determine if they are
  Member of target population
  Physically accessible
  Landowner permission to sample
Four step evaluation is typical
  Office assessment based on existing information
  Phone call to knowledgeable local person
  Field reconnaissance visit
  Field visit to sample the spatial unit
Evaluation results recorded for all spatial units evaluated
Measurements recorded only for spatial units sampled

## Slide 9: Spatial Unit Evaluation Status
Critical that know what happened to each site selected by the design
  Ensures that we know how the design was implemented
  Use information to adjust weights for statistical analysis
  Use to estimate the extent (size) of the sampled population
Evaluation Status codes (example)
  TS: Target Sampled
  LD: Landowner Denied Access
  PB: Physically inaccessible
  NT: Non-Target
  NS: Target Not Sampled
  NN: Not Needed

## Slide 10: Incorporating Spatial Unit Evaluation Information in Design File
Design
File
Site
Evaluation:
Office &
Field Recon
Implemented
Design
File
Adjust
Weight
Process
Sample Frame
Summary

## Slide 11: Implemented Design File Contents: Has all sites selected by survey design
Site Identification
  Site ID
  Latitude/Longitude
Auxiliary Frame Information
  Site Name
  Sample Frame ID
  County
  Map names
  State
  Omernik Ecoregion
  Other
Survey Design
  Stratum
  Panel
  Over sample
  Multi-Density Category
  Initial Weight
  Adjusted Weight
  Adjusted Weight Categories
Site Evaluation
  Evaluation Status
  Evaluation Reason
Notes: Black: information in original design file
Green: information from site evaluation process
Red: information to record the implemented design weights and adjustment categories

## Slide 12: Adjust Weights: adjwgt
Sites: column indicating which sites to use (True/False)
  All sites evaluated should be included (True)
  Sites not evaluated should be excluded (False)
Weights: column of weights to be adjusted
Weight categories: category each site belongs to for the weight adjustment
  Categories depend on how sites were selected to be evaluated
  Sites must be evaluated in “siteID” order within a category
Framesize: For each weight category the size of the sample frame

## Slide 13: Population Extent Estimation

## Slide 14: Population Extent Estimation: cat.analysis
Sites data frame that specifies which sites will be used in the population estimation
Sub-population data frame that specifies site membership in each Reporting Domain for which population estimates will be computed
Design data frame that specifies the spatial survey design information for each site
Data (categorical) data frame that includes evaluation status data for which population estimates will be computed
Options are available to specify variance estimator to be used, if population size is known, confidence level desired, etc

## Slide 15: Extent Estimation: Three Cases
  Target and non-target population extent in sample frame
    Use all spatial units evaluated (True)
    Categorize evaluation status as Target, NonTarget or Unknown
    Specify known population size (popsize)
  Target population sampled (sampled population) extent
    Use only spatial units evaluated as Target (True)
    Use evaluation status categories as data
    Do not specify population size (not known)
  Non-target population extent in sample frame by reason why non-target
    Use only spatial units evaluated as NonTarget (True)
    Use evaluation status categories as data
    Do not specify population size (not known)

## Slide 16: Population Estimation for Indicators on Reporting Domains

## Slide 17: Category Analyses: cat.analysis
Sites data frame that specifies which sites will be used in the population estimation
Sub-population data frame that specifies site membership in each Reporting Domain for which population estimates will be computed
Design data frame that specifies the spatial survey design information for each site
Data (categorical) data frame that includes each metric for which population estimates will be computed
Options are available to specify variance estimator to be used, if population size is known, confidence level desired, etc

## Slide 18: Continuous Data Analyses: cont.analysis
Sites data frame that specifies which sites will be used in the population estimation
Sub-population data frame that specifies site membership in each Reporting Domain for which population estimates will be computed
Design data frame that specifies the spatial survey design information for each site
Data (categorical) data frame that includes each metric for which population estimates will be computed
Options are available to specify variance estimator to be used, if population size is known, confidence level desired, etc

## Slide 19: CDF Plots: cont.cdfplot
This function creates CDF plots suitable for a quick review of continuous data population estimates
Input data for the plots is provided by a data frame utilizing the same structure as the data frame named "CDF" that is included in the output object produced by function cont.analysis
Plots are produced for every combination of Type of population, subpopulation within Type, and indicator
Output from the function is placed in a PDF file.

## Slide 20: Test for Differences between two CDFs: cont.cdftest
This function organizes input and output for conducting inference regarding cumulative distribution functions (CDFs) generated by a probability survey
Input similar to cont.analysis
Results are CDF test results for all pairs of Reporting Domains specified for every metric provided
Test statistic is the F distribution version of the Wald statistic
Test statistic procedures divide the CDFs into a discrete set of intervals (classes) and then utilize procedures that have been developed for analysis of categorical data from probability surveys

## Slide 21: Relative Risk Estimates: relrisk.analysis
Sites data frame that specifies which sites will be used in the population estimation
Sub-population data frame that specifies site membership in each Reporting Domain for which population estimates will be computed
Design data frame that specifies the spatial survey design information for each site
Relative Risk metric data frame that includes categorical response metrics and categorical stressor metrics for which population estimates will be computed
Response and stressor category levels used in relative risk calculations